## Slide 1: Special Projects Team

## Slide 2: Overview
Special Projects Team
PackML
SPT Framework
Github.com

## Slide 3: SPT Team Background
Formed in 2021
To formalize and control projects that Beckhoff takes on
To develop, formalize and control the tools and framework for TwinCAT programming in various industries
Implement good coding practice and framework on customer machines

## Slide 4: SPT Group
What We Provide....
9 highly experienced software engineers who are very familiar with the use and application of Beckhoff products. (150 years of cumulative experience).
Help Establish requirement specification
On the job technical training of software development and hardware
Supporting documentation
Sign off acceptance
Controlled and collaborative software & documentation repository (Azure DevOps)
Work with local Application Engineers to fulfill requirements
Framework to build applications

## Slide 5: PackML - OMAC
What is PackML?
Benefits of PackML

## Slide 6: PackML – Our View
3 major topics in PackML
  State Engine – Run Machine and Equipment Modules
  PackTags – Communication to outside
  Programming Methodology
    Machine Module / Equipment module / Component

## Slide 7: PackML State Engine
17 States
32 modes
All configurable
  Can use as little as one mode and 5 states
We support the use of all modes and states

## Slide 8: PackML PackTags
Tags define how the program communicates with other machines and higher-level control systems
3 Types of tags
  Command – Used by the machine to make a change from outside
  Status – Written by machine to be used elsewhere
    Current State, Current Mode, etc..
  Admin – Used for analysis, operator information and units produced
    Data needed for OEE – State Times, products produced, defective, etc…
    Stop Reason, Last 10 Alarms

## Slide 9: PackML Machine Module / Equipment Module / Component
Machine (Unit)
  An entire machine – Filler, Capper, Wrapper, etc..
Equipment Module
  A station or section of machine – Infeed, filler, outfeed, etc..
Component(Control Module)
  An actuator or piece of equipment – Servo, VFD, Sensor, etc..
An application can also just be a Machine Module and some Components

## Slide 10: PackML Implementations
2 ways to implement
  Intermediate interface to existing PLC code and translate local states to PackML Tags and PackML definitions
  Run machine using PackML State Engine and Machine / Equipment / Component method and PackML Tags
We wrap the PackML overhead into our framework so you can put your effort into application programming.

## Slide 11: SPT Framework - Overview
Template PLC project
  Machine Module Function Block(FB)
  Template FB for Equipment Modules
Template HMI starter project
  Header
  Navigation
  Start/Stop/Reset
  Content Area
  Alarm Notification & Display
  SPT user controls
Set of Libraries to support the modules and components
Code uses Object Oriented Programming(OOP) methodology in Structured Text
Notes: Show the libraries in TwinCAT or Beckhoff-USA-Community

## Slide 12: SPT Framework – Base Types
FB_BaseFB
  Properties: Busy, Error, ErrorID
  Methods for Tracing Messages
FB_CyclicFB
  Property: InitComplete
  Method CyclicLogic
  Extends FB_BaseFB

## Slide 13: SPT Framework – PackML Base
The Machine module and Equipment module are based on the FB_PackML_BaseModule that extends FB_CyclicFB
This base code handles the Mode/State changes
Handles the raising of alarms to the parent
All states have a base functionality that can be overriden in a module
HMI tags for integration with HMI User Controls
Calls all the subModules CyclicLogic and Components CyclicLogic

## Slide 14: SPT Framework - Components
A component is an extension on the FB_ComponentBase
A component is the connection between the software and hardware
Components can be in the machine module or any equipment module
We have a wide range of predefined components from Axes to device specific components like a FanucRobot interface
Many others and the library of components is growing

## Slide 15: Alarms with TwinCAT Event Logger
The TwinCAT built in Event Logger is used for Alarming
5 levels of severity: verbose, info, warning, error, critical
TwinCAT HMI can be easily integrated
Configurable reaction to alarms at equipment and machine module
Alarms are used to fill the Pack Tags

## Slide 16: GIT Hub
Beckhoff USA · GitHub
  SPT Libraries – link
  VFFS Demo
    PackML_PLC_Example - link
    PackML_HMI_Example - link

## Slide 17: Questions ?

## Slide 20
03/2022